## Slide 1: UART(Universal Asynchronous Receiver and Transmitter)
Presented by
Boddu Giresh
ChipWeave Technologies Pvt Ltd

## Slide 2: Introduction
UART(Universal Asynchronous Receiver/Transmitter)
Used for serial communication
It is two wire commnuication protocol
One wire for transmission
Second wire for reception
Here ,no clock
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 3: UART Communication – Frame Structure
Data is transferred bit-by-bit using a predefined frame format
A UART frame consists of:
Start Bit
Data Bits (5–9 bits, typically 8)
Parity Bit (Optional)
Stop Bit
Notes: Lesson descriptions should be brief.

## Slide 4: Registers list
Name | Width | Access | Description
Receiver Buffer | 8 | R | Receiver FIFO output
Transmitter Holding Register (THR) | 8 | W | Transmit FIFO input
Interrupt Enable Register (IER) | 8 | RW | Enable/Mask interrupts generated by the UART
Interrupt Identification Register (IIR) | 8 | R | Provides interrupt source information
FIFO Control Register (FCR) | 8 | W | Controls FIFO options
Line Control Register (LCR) | 8 | RW | Controls line configuration
Modem Control Register (MCR) | 8 | W | Controls modem signals
Notes: Example objectives
At the end of this lesson, you will be able to:
Save files to the team Web server.
Move files to different locations on the team Web server.
Share files on the team Web server.

## Slide 5: Registers list
Name | Width | Access | Description
Line Status Register (LSR) | 8 | R | Provides line status information
Modem Status Register (MSR) | 8 | R | Modem Status Register (MSR)
Notes: Example objectives
At the end of this lesson, you will be able to:
Save files to the team Web server.
Move files to different locations on the team Web server.
Share files on the team Web server.

## Slide 6: Interrupt Enable Register (IER)
This register enables or disables interrupt generation by the UART.
Bit # | Access | Description
0 | RW | Received Data Available Interrupt 0 = Disabled,1 = Enabled
1 | RW | Transmitter Holding Register Empty Interrupt 0 = Disabled,1 = Enabled
2 | RW | Receiver Line Status Interrupt 0 = Disabled,1 = Enabled
3 | RW | Receiver Line Status Interrupt 0 = Disabled,1 = Enabled
7-4 | RW | Reserved (Must be written as logic 0)

## Slide 7: Interrupt Identification Register(IIR)
The IIR enables the programmer to retrieve what is the current highest priority pending interrupt.
Bit 3 | Bit 2 | Bit 1 | Priority | Interrupt Type | Interrupt Source | Interrupt Reset Control
0 | 1 | 1 | 1st | Receiver Line Status | Parity, Overrun or Framing errors or Break Interrupt | Reading the Line Status Register
0 | 1 | 0 | 2nd | Receiver Data available | FIFO trigger level reached | FIFO drops below trigger level
1 | 1 | 0 | 3rd | Timeout Indication | RX FIFO has data No new data received or read for 4 character times | Reading from the FIFO (Receiver Buffer Register)
0 | 0 | 1 | 4th | Transmitter Holding Register empty | Transmitter Holding Register Empty | Writing to the Transmitter Holding Register or reading IIR.
0 | 0 | 0 | 5th | Modem Status | CTS, DSR, RI or DCD. | Reading the Modem status register.

## Slide 8: FIFO Control Register (FCR)
The FCR allows selection of the FIFO trigger level (the number of bytes in FIFO required to enable the Received Data Available interrupt).
Bit # | Access | Description
0 | W | Ignored (Used to enable FIFOs in NS16550D). Since this UART only supports FIFO mode, this bit is ignored.
1 | W | Clears Receiver FIFO Writing 1 → clears RX FIFO and resets its internal logic Shift register not cleared, i.e., the byte currently being received continues normally
2 | W | Clears Transmitter FIFO Writing 1 → clears TX FIFO and resets its logic Shift register not cleared, so the byte currently being transmitted continues
5-3 | W | Ignored
7-6 | W | Define the Receiver FIFO Interrupt trigger level ‘00’ – 1 byte ‘01’ – 4 bytes ‘10’ – 8 bytes ‘11’ – 14 bytes

## Slide 9: Line Control Register (LCR)
The line control register allows the specification of the format of the asynchronous data communication used.
Bit # | Access | Description
1-0 | RW | Select number of bits in each character ‘00’ – 5 bits, ‘01’ – 6 bits, ‘10’ – 7 bits ‘11’ – 8 bits
2 | RW | Specify the number of generated stop bits '0' - 1 stop bit '1' - 1.5 stop bits (only if 5-bit data) '1' - 2 stop bits (for 6/7/8-bit data)
3 | RW | Parity Enable ‘0’ – No parity ‘1’ – Parity bit If enabled: Transmitter adds parity bit Receiver checks parity bit

## Slide 10: Line Control Register (LCR)
Bit # | Access | Description
4 | RW | Even Parity Select Selects odd or even parity (only valid if parity enabled). '0' - Odd parity '1' - Even parity
5 | RW | Stick Parity Forces parity bit to a fixed value. ‘0’ – Stick Parity disabled ‘1’ - Stick parity enabled
6 | RW | Break Control Forces TX line to logic 0 continuously. '0' - Normal operation '1' - TX line forced LOW (Break condition)
7 RW Divisor Latch Access bit. ‘1’ – The divisor latches can be accessed ‘0’ – The normal registers are accessed

## Slide 11: Modem Control Register (LCR)
Modem Control Register (MCR) controls handshaking signals between UART and a modem
Bit # | Access | Description
0 | W | DTR (Data Terminal Ready) Control Signal '0' - DTR output = 1 (UART is ready) '1' - DTR output = 0
1 | W | RTS (Request To Send) control signal '0' - RTS output = 1(UART asks Modem) '1' - RTS output = 0
2 | W | Out1. In loopback mode, connected Ring Indicator (RI) signal input
3 | W | Out2. In loopback mode, connected to Data Carrier Detect (DCD) input.

## Slide 12: Modem Control Register (LCR)
Bit # | Access | Description
4 | W | Loopback mode ‘0’ – normal operation ‘1’ – loopback mode. When in loopback mode, UART tests itself No external modem needed Transmitter output internally connected to receiver input The following connections are made: DTR -> DSR RTS -> CTS Out1 ->RI Out2 -> DCD
7-5 | W | Ignored

## Slide 13: Line Status Register (LSR)
Line Status Register (LSR) tells the current status of UART transmission and reception:
#Bit | Access | Description
0 | R | DR (Data Ready) Indicates received data availability. '0' - No data in RX FIFO '1' - At least one byte is available in RX FIFO
1 | R | OE (Overrun Error) RX FIFO overflow detection. '1' - FIFO full and new data arrived → data loss '0' - No overrun
2 | R | PE (Parity Error) Parity check error detection. '1' - Parity error in received character '0' - No parity error

## Slide 14: Line Status Register (LSR)
3 | R | FE (Framing Error) Stop-bit error detection '1' - Stop bit is invalid or missing '0' - Stop bit correct
4 | R | BI (Break Interrupt) Detects long LOW condition on RX line. '1'- Line held LOW longer than one frame '0' - No break condition
5 | R | Transmit FIFO is empty. TX FIFO status. '1' - TX FIFO empty '0' - TX FIFO has data
6 | R | Transmitter Empty indicator. '1' - TX FIFO and shift register empty '0' - Transmission still in progress
7 | R | Error in FIFO ,Error summary bit. '1' - At least one error in RX FIFO(Parity error, Framing error ,Break error) '0' - No errors

## Slide 15: Modem Status Register (MSR)
Current state of modem control lines
Whether those signals have changed since the last read
Bit # | Access | Description
0 | R | DCTS (Delta Clear To Send) Detects change in CTS signal. '1' - CTS line changed (0→1 or 1→0) '0' - No change
1 | R | DDSR (Delta Data Set Ready) Detects change in DSR signal. '1' - DSR line changed '0' - No change
2 | R | TERI (Trailing Edge Ring Indicator) Detects falling edge of RI signal. '1'- RI changed from HIGH → LOW '0' - No falling edge

## Slide 16: Modem Status Register (MSR)
3 | R | DDCD (Delta Data Carrier Detect) Detects change in DCD signal. '1' - DCD line changed '0' - No change
4 | R | Complement of the CTS input or equals to RTS in loopback mode.
5 | R | Complement of the DSR input or equals to DTR in loopback mode.
6 | R | Complement of the RI input or equals to Out1 in loopback mode.
7 | R | Complement of the DCD input or equals to Out2 in loopback mode.

## Slide 17: THANK YOU

## Slide 18
parameter | UART | SPI | I2C
clock | No (Asynchronous) | synchronous | synchronous
wires | 2 | 4 | 2
speed | 1-2mbps | 10-100mbps | 3.4mbps
Addressing | no | Limited(cs) | yes
communication | Point –to-point | Master-slave | Master-slave
Use case | Gps module ,bluetooth | displays | sensors

## Slide 19: Questions
1)find over header precentage?
Start bit =1,data bits=8,stop bit=1
1A)total bits =10,overheader bits =2
Overheader precentage = 20%
2)what is baudrate and bitrate?
2A)Baudrate = the no of signal changes per second
Bitrate = the no of data bits transfer per second
3) what are the errors in i2c?
3A)parity error,framing error,break error,overrun error(RX fifo over flow)
4) what is the method used error detection?
4A) parity bit used error detection