## Slide 1
CXS( CREDITED EXTENSIBLE STREAM)
Boddu Giresh
CHIPWEAVE TECHNOLOGIES PVT LTD

## Slide 2
ABOUT THE CXS STREAMING INTERFACE PROTOCOL
  CXS is a high-speed, low-latency, streaming interface protocol mainly used for die-to-die communication, NoC connectivity, and chiplet architectures. It is designed to move large amounts of data efficiently between blocks, IPs, or chiplets, similar in nature to AMBA CHI streaming, AXI-Stream, or PIPE interfaces.
  High bandwidth with scalable data width (32 to 1024 bits)
  Low latency, minimal overhead
  Supports packetized and raw streaming data
  Supports flow control, backpressure, credits
  Designed for multi-die / chiplet interconnects
  Works with high-speed PHY (like BoW, UCIe, proprietary interfaces)
MAIN GOALS OF CXS

## Slide 3
MANDATORY AND OPTIONAL CXS SIGNALS

## Slide 4
CXS PACKETS
  The data that is transmitted on the CXS interface is organized into packets. When the property CXSMAXPKTPERFLIT is greater than 1, there can be multiple packets per flit. This chapter describes how multiple packets are packed into a CXS flit. In CCIX or PCIe terminology, this is a Transaction Layer Packet (TLP).
The CXS packets are described in the following sections
  Packet Position Constraints
  Packet Control Signal
  Packet Size Constraints
  Packet Examples

## Slide 5
PACKET POSITION CONSTRAINTS
CXSMAXPKTPERFLIT specifies the maximum number of packets that can have bytes in a flit. There can be up to CXSMAXPKTPERFLIT new packets starting in a flit, and up to CXSMAXPKTPERFLIT packets ending in a flit. This defines the maximum packets per flit, including any packet started in previous flits and any packet started in this flit which will be completed in subsequent flits.
When CXSMAXPKTPERFLIT is greater than 1:
• The first byte of a packet must be placed on an aligned 16-byte boundary.
• Subsequent bytes of the packet occupy subsequent bytes of the flit.
• Packets can end on any four-byte aligned boundary.
• The packet that starts at a byte position will occupy every subsequent byte in that flit until the packet ends or the flit ends.
• If there are remaining bytes in the packet when the flit ends, that packet will start at byte[0] of the next flit and occupy every subsequent byte position until the packet ends or the flit ends.
• When a packet ends within a flit, the remaining bytes in the flit can be unused.
• Any packet in a flit must begin at the first available 16-byte boundary relative to the start of the flit or the ending of a previous packet
When CXSMAXPKTPERFLIT is 1:
• Packets start on the first byte of CXSDATA.
• Packets end on the last byte of CXSDATA.
• Packets do not span across multiple flits

## Slide 6
PACKET CONTROL SIGNAL
The control fields of a CXS packet are signaled using CXSCNTL. This section describes the fields and positioning within the CXSCNTL signal
The CXSCNTL signal contains five fields. The widths of each field, and therefore the bit position of each field, vary with the properties of the interface
PACKET CONTROL FIELDS
1.START Field
  Indicates how many packets start in the current flit.
  Width = CXSMAXPKTPERFLIT.
  Rule: If START[N] = 1, then all lower bits START[N-1:0] must be 1.
  Example (CXSMAXPKTPERFLIT = 4):
    START[0] = 1 → at least 1 packet starts
    START[1] = 1 → at least 2 packets start
    START[2] = 1 → at least 3 packets start
    START[3] = 1 → at least 4 packets start

## Slide 7
3.END Field
  Indicates how many packets end in this flit.
  Width = CXSMAXPKTPERFLIT.
  Rule: If END[N] = 1, all lower bits END[N-1:0] must be 1.
  Example (CXSMAXPKTPERFLIT = 4):
    END[0] = 1 → 1 packet ends
    END[1] = 1 → 2 packets end
    END[2] = 1 → 3 packets end
    END[3] = 1 → 4 packets end
2.START[N]PTR (Start Pointer)
  Array of pointers for packet start positions inside the flit.
  Pointer valid only if matching START[N] = 1.
  All packet starts are 16-byte aligned.
  Pointer width = log₂(CXSDATAFLITWIDTH / 128) bits.
  Actual start byte = (START[N]PTR << 4).
  Pointers must be monotonically increasing
  (START1PTR > START0PTR).

## Slide 8
4.ENDERROR Field
  Indicates error on packets ending in this flit.
  Width = same as END.
  ENDERROR[N] = 1 → Nth ending packet has error.
  Rule: If ENDERROR[N] = 1, then END[N] must be 1.
5.END[N]PTR (End Pointer)
  Pointer to the last 4 bytes of packet ending in this flit.
  Valid only if END[N] = 1.
  All packet ends are 4-byte aligned.
  Pointer width = log₂(CXSDATAFLITWIDTH / 32) bits.
  Actual last byte = ((END[N]PTR << 2) + 3).
  Pointers must be monotonically increasing
  (END1PTR > END0PTR).

## Slide 9
PACKET CONTROL FIELD STRUCTURE
CXSMAXPKTPERFLIT = 2, CXSDATAFLITWIDTH = 256

## Slide 10
PACKET SIZE CONSTRAINTS
A CXS interface transmits packets of data that meet the following requirements:
• At least 4 bytes in size
• A multiple of 4 bytes in size
• No upper limit on packet size

## Slide 11
TEAM MEMBERS
MEET OUR
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore

## Slide 12
FLOW CHART
OUR YEARLY
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore

## Slide 13
DETAILS 2
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore

## Slide 14
PLANNING
OUR NEW
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore

## Slide 15
THANK YOU
VISIT US
www.reallygreatsite.com
+123-456-7890