## Slide 1
CXS( CREDITED EXTENSIBLE STREAM)
Boddu Giresh
CHIPWEAVE TECHNOLOGIES PVT LTD

## Slide 2
ABOUT THE CXS STREAMING INTERFACE PROTOCOL
  CXS is a high-speed, low-latency, streaming interface protocol mainly used for die-to-die communication, NoC connectivity, and chiplet architectures. It is designed to move large amounts of data efficiently between blocks, IPs.
  High bandwidth with scalable data width (32 to 1024 bits)
  Low latency, minimal overhead
  Supports packetized and raw streaming data
  Supports flow control, backpressure, credits
  Designed for multi-die / chiplet interconnects
  Works with high-speed PHY (like BoW, UCIe, proprietary interfaces)
MAIN GOALS OF CXS

## Slide 3
MANDATORY AND OPTIONAL CXS SIGNALS

## Slide 4
CXS PACKETS
  The data that is transmitted on the CXS interface is organized into packets. When the property CXSMAXPKTPERFLIT is greater than 1, there can be multiple packets per flit. This chapter describes how multiple packets are packed into a CXS flit. In CCIX or PCIe terminology, this is a Transaction Layer Packet (TLP).
The CXS packets are described in the following sections
  Packet Position Constraints
  Packet Control Signal
  Packet Size Constraints
  Packet Examples

## Slide 5
PACKET POSITION CONSTRAINTS
CXSMAXPKTPERFLIT specifies the maximum number of packets that can have bytes in a flit. There can be up to CXSMAXPKTPERFLIT new packets starting in a flit, and up to CXSMAXPKTPERFLIT packets ending in a flit. This defines the maximum packets per flit, including any packet started in previous flits and any packet started in this flit which will be completed in subsequent flits.
When CXSMAXPKTPERFLIT is greater than 1:
• The first byte of a packet must be placed on an aligned 16-byte boundary.
• Subsequent bytes of the packet occupy subsequent bytes of the flit.
• Packets can end on any four-byte aligned boundary.
• The packet that starts at a byte position will occupy every subsequent byte in that flit until the packet ends or the flit ends.
• If there are remaining bytes in the packet when the flit ends, that packet will start at byte[0] of the next flit and occupy every subsequent byte position until the packet ends or the flit ends.
• When a packet ends within a flit, the remaining bytes in the flit can be unused.
• Any packet in a flit must begin at the first available 16-byte boundary relative to the start of the flit or the ending of a previous packet
When CXSMAXPKTPERFLIT is 1:
• Packets start on the first byte of CXSDATA.
• Packets end on the last byte of CXSDATA.
• Packets do not span across multiple flits

## Slide 6
PACKET CONTROL SIGNAL
The control fields of a CXS packet are signaled using CXSCNTL. This section describes the fields and positioning within the CXSCNTL signal
The CXSCNTL signal contains five fields. The widths of each field, and therefore the bit position of each field, vary with the properties of the interface
PACKET CONTROL FIELDS
1.START Field
  Indicates how many packets start in the current flit.
  Width = CXSMAXPKTPERFLIT.
  Rule: If START[N] = 1, then all lower bits START[N-1:0] must be 1.
  Example (CXSMAXPKTPERFLIT = 4):
    START[0] = 1 → at least 1 packet starts
    START[1] = 1 → at least 2 packets start
    START[2] = 1 → at least 3 packets start
    START[3] = 1 → at least 4 packets start

## Slide 7
3.END
  Indicates how many packets end in this flit.
  Width = CXSMAXPKTPERFLIT.
  Rule: If END[N] = 1, all lower bits END[N-1:0] must be 1.
  Example (CXSMAXPKTPERFLIT = 4):
    END[0] = 1 → 1 packet ends
    END[1] = 1 → 2 packets end
    END[2] = 1 → 3 packets end
    END[3] = 1 → 4 packets end
2.START[N]PTR (Start Pointer)
  Array of pointers for packet start positions inside the flit.
  Pointer valid only if matching START[N] = 1.
  All packet starts are 16-byte aligned.
  Pointer width = log₂(CXSDATAFLITWIDTH / 128) bits.
  Actual start byte = (START[N]PTR << 4).
  Pointers must be monotonically increasing
  (START1PTR > START0PTR).

## Slide 8
4.ENDERROR
  Indicates error on packets ending in this flit.
  Width = same as END.
  ENDERROR[N] = 1 → Nth ending packet has error.
  Rule: If ENDERROR[N] = 1, then END[N] must be 1.
5.END[N]PTR (End Pointer)
  Pointer to the last 4 bytes of packet ending in this flit.
  Valid only if END[N] = 1.
  All packet ends are 4-byte aligned.
  Pointer width = log₂(CXSDATAFLITWIDTH / 32) bits.
  Pointers must be monotonically increasing
  (END1PTR > END0PTR).

## Slide 9
PACKET CONTROL FIELD STRUCTURE
CXSMAXPKTPERFLIT = 2, CXSDATAFLITWIDTH = 256

## Slide 10
PACKET SIZE CONSTRAINTS
A CXS interface transmits packets of data that meet the following requirements:
• At least 4 bytes in size
• A multiple of 4 bytes in size
• No upper limit on packet size
1
2
3
4
5
6
7
9
8
10
12
11
13
0
start
END1PTR
END0PTR
END ERROR
END
s1p
s0p

## Slide 11
INTERFACE CONTROL WITH EXPLICIT CREDIT RETURN
  A CXS interface can be optionally configured to include signaling for activation and deactivation, using the CXSLINKCONTROL property. The property can be set to None or Explicit_Credit_Return. When the CXSLINKCONTROL property is set to None, there are no signals for interface activation and deactivation. This setting requires that the Receiver must always send credits when they are available, and the Transmitter must always be able to receive them.
CXSCRDRTN – Credit Return
  Direction: Transmitter → Receiver
  Returned when transmitter does NOT use a previously granted credit
  Can be asserted only when CXSVALID = 0
  Helps receiver reuse credits early and maintain flow control efficiency
CXSACTIVEREQ – Link Activation Request
  Direction: Transmitter → Receiver
  Used to request activation or deactivation of the CXS link
  Initiates link state transitions (STOP → ACTIVATE → RUN)
SIGNALS FOR LINK CONTROL USING EXPLICIT CREDIT RETURN

## Slide 12
CXSDEACTHINT – Deactivation Hint
  Direction: Receiver → Transmitter
  Receiver indicates it would like the link to be deactivated soon
  Used for power saving or idle-time optimization
  Does not force deactivation — transmitter decides when safe
CXSACTIVEACK – Link Activation Acknowledge
  Direction: Receiver → Transmitter
  Confirms the transmitter's activation/deactivation request
  Ensures both sides remain in the same link state

## Slide 13
REQUEST AND ACKNOWLEDGMENT HANDSHAKING
  Request and acknowledge handshaking uses CXSACTIVEREQ and CXSACTIVEACK as primary signals.
FOUR STATES ARE DEFINED FOR THE INTERFACE OPERATION:
  stop state
  Active state
  Run state
  Deactive State

## Slide 14
THANK YOU

## Slide 16
PLANNING
OUR NEW
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore