## Slide 1
JTAG
presented by
BODDU GIRESH
CHIPWEAVE TECHNOLOGIES PVT LTD

## Slide 2
WHAT IS JTAG?
  JTAG stands for Joint Test Action Group.
  It is a standard test access port (TAP) and boundary scan architecture.
  Used for testing interconnects on PCBs.
  Enables debugging, programming, and testability of ICs.
  Defined under IEEE 1149.1 standard.
  Testing PCB connections
  Detecting shorts & opens
  Programming devices
  On-chip debug
  Boundary scan testing
WHY JTAG IS NEEDED

## Slide 3
JTAG USES TESt Access Port (TAP) Pins
Four Mandatory Pins:
  TDI – Test Data In
  TDO – Test Data Out
  TCK – Test Clock
  TMS – Test Mode Select
5. TRST – Test Reset
1. JTAG sends control signals to TAP
  TCK gives clock pulses.
  TMS selects next state of the TAP Controller FSM.
2. TAP Controller enters different states
  TAP Controller is a 16-state FSM that controls:
  Loading instruction (IR path)
  Loading/shifting test data (DR path)

## Slide 4
3. JTAG shifts data through TDI → TAP → TDO
Depending on state:
  TAP shifts instruction bits into IR
  TAP shifts data bits into DR (boundary scan, IDCODE, BYPASS)
4. TAP executes JTAG Instructions
Examples:
  EXTEST → test PCB connections
  INTEST → test internal logic
  SAMPLE → capture pin values
  IDCODE → read device ID
The TAP controller selects which Data Register is active.
5. TAP applies data to Boundary Scan Cells
  TAP drives/controls every boundary scan cell in the chain
  Used for:
    Testing pins
    Capturing logic levels
    Driving test patterns

## Slide 5
JTAG ARCHITECTURE DIAGRAM (BOUNDARY SCAN)
Interface Signals
The JTAG interface, collectively known as a Test Access Port, or TAP, uses the following signals to support the operation of boundary scan.
  TCK (Test Clock) – this signal synchronizes the internal state machine operations.
  TMS (Test Mode Select) – this signal is sampled at the rising edge of TCK to determine the next state.
  TDI (Test Data In) – this signal represents the data shifted into the device’s test or programming logic. It is sampled at the rising edge of TCK when the internal state machine is in the correct state.
  TDO (Test Data Out) – this signal represents the data shifted out of the device’s test or programming logic and is valid on the falling edge of TCK when the internal state machine is in the correct state.
  TRST (Test Reset) – this is an optional pin which, when available, can reset the TAP controller’s state machine.
  Schematic Diagram of a JTAG enabled device.

## Slide 6
TARGET 1
TARGET 1
TARGET 1
There are two types of registers associated with boundary scan. Each compliant device has one instruction register and two or more data registers.
Instruction Register – the instruction register holds the current instruction. Its content is used by the TAP controller to decide what to do with signals that are received. Most commonly, the content of the instruction register will define to which of the data registers signals should be passed.
Data Registers – there are three primary data registers, the Boundary Scan Register (BSR), the BYPASS register and the IDCODES register. Other data registers may be present, but they are not required as part of the JTAG standard.
  BSR – this is the main testing data register. It is used to move data to and from the I/O pins of a device.
  BYPASS – this is a single-bit register that passes information from TDI to TDO. It allows other devices in a circuit to be tested with minimal overhead.
  IDCODES – this register contains the ID code and revision number for the device. This information allows the device to be linked to its Boundary Scan Description Language (BSDL) file. The file contains details of the Boundary Scan configuration for the device.
REGISTERS

## Slide 7
  All states have two exits, so all transitions can be controlled by the single TMS signal sampled on TCK. The two main paths allow for setting or retrieving information from either a data register or the instruction register of the device. The data register operated on (e.g. BSR, IDCODES, BYPASS) depends on the value loaded into the instruction register.
  The TAP controller, a state machine whose transitions are controlled by the TMS signal, controls the behaviour of the JTAG system
TEST ACCESS PORT (TAP) CONTROLLER

## Slide 8
MARKETING
STRATEGY
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
presented by
Alfredo Torez

## Slide 9
OUR TEAM
PROJECT MANAGER
OLIVIA WILSON
BUSINESS ANALYST
CLAUDIA ALVES
UI / UX ENGINEER
ALFREDO TOREZ
presented by
Alfredo Torez

## Slide 10
GET IN
TOUCH
EMAIL
ADDRESS
PHONE
WEBSITE
hello@reallygreatsite.com
123 Anywhere St., Any City, ST 12345
+123-456-7890
reallygreatsite.com
presented by
Alfredo Torez