## Slide 1: JTAG (IEEE 1149.1)
Joint Test Action Group
Boundary Scan & Test Access Port

## Slide 2: What is JTAG?
• JTAG stands for Joint Test Action Group
• Standard test access & boundary scan architecture
• Used for testing, debugging, and programming ICs and PCBs
• Defined under IEEE 1149.1

## Slide 3: Why JTAG is Needed
• IC complexity makes probing internal signals difficult
• High-density packages like BGA/QFN limit access
• JTAG enables:
- PCB interconnect testing
- Debugging
- Device programming
- Fault isolation

## Slide 4: JTAG Applications
• Boundary Scan Testing
• On-chip Debug
• Firmware downloading
• FPGA configuration
• Flash/Memory programming
• Production testing

## Slide 5: JTAG Pins (TAP Interface)
Mandatory Pins:
• TDI - Test Data In
• TDO - Test Data Out
• TCK - Test Clock
• TMS - Test Mode Select
Optional:
• TRST - Test Reset

## Slide 6: Boundary Scan Architecture
• TAP Controller
• Instruction Register (IR)
• Data Registers:
- Boundary Scan Register
- Bypass Register
- IDCODE Register
• TDI → Register chain → TDO

## Slide 7: Boundary Scan Basics
• Each I/O pin has a Boundary Scan Cell (BSC)
• BSC can capture and override pin values
• Enables PCB testing without physical probing

## Slide 8: Common JTAG Instructions
• BYPASS – bypass register
• EXTEST – external interconnect test
• SAMPLE/PRELOAD – sample or preload values
• IDCODE – read device ID
• INTEST – internal logic test

## Slide 9: TAP Controller State Machine
• 16-state FSM
• Driven by TCK and TMS
• IR and DR paths for shifting instructions/data

## Slide 10: Advantages of JTAG
• Non-invasive testing
• Low test cost
• Supports debug & programming
• Internal access without probing
• Essential for modern IC testing

## Slide 11: Industry Usage
• ASIC/FPGA debugging
• Board bring-up
• Production test
• Tools: Vivado, Quartus, OpenOCD, J-Link, Lauterbach

## Slide 12: Summary
• JTAG = IEEE 1149.1 boundary scan standard
• Provides test, debug & programming access
• Uses TAP + boundary scan cells
• Critical for DFT & PCB testing