## Slide 1: Reset Domain Crossing (RDC)
Concept, Issues, and Synchronizer Solution

## Slide 2: What is Reset Domain Crossing (RDC)?
• RDC occurs when signals cross between flip-flops using different reset signals.
• Even if both flip-flops use the same clock, differing resets create unsafe crossings.
• This can cause metastability, glitches, and functional failures.

## Slide 3: Why RDC Happens
• Reset A may de-assert at a different time than Reset B.
• One flip-flop becomes active earlier and starts toggling while the other is still in reset.
• When the second flop comes out of reset, it samples unstable data.

## Slide 4: Metastability in RDC
• Setup or hold violation occurs when flop samples data in transition.
• Output becomes unpredictable (between 0 and 1).
• Can propagate errors and cause system failure.

## Slide 5: Solution: Reset De-assertion Synchronizer
• Use two flip-flops to synchronize reset release into clock domain.
• Ensures clean reset removal.
• Avoids metastability at reset release.

## Slide 6: Reset Synchronizer Code
always_ff @(posedge clk or negedge rst_async)
if (!rst_async) sync1 <= 1'b0;
else sync1 <= 1'b1;
always_ff @(posedge clk or negedge rst_async)
if (!rst_async) sync2 <= 1'b0;
else sync2 <= sync1;
assign rst_sync = sync2;