## Slide 1
SERIAL PERIPHERAL INTERFACE(SPI)
Presented by Giresh,Lokesh
Chipweave Technologies Pvt Ltd

## Slide 2
INTRODUCTION TO SPI
  SPI supports half-duplex and full-duplex serial communication.
  It is a synchronous communication protocol (clock is provided along with data).
  SPI is a four-wire communication protocol.
  In most cases, SPI uses a single master and multiple slave configuration, but it also supports multiple master configurations.
  SPI is an on-board, short-range communication protocol used in embedded systems.
  It supports high-speed data transfer, typically up to 10 Mbps.
  The master provides the clock for synchronization.
  SPI supports 8-bit and 16-bit data frame formats.

## Slide 3
SCLK – serial clock, generated by the master
MOSI –master output/slave input
MISO –master input/slave output
SS – slave select/enable signal
SPI CONNECTIONS

## Slide 4
Master selects the slave
  The master pulls SS (Slave Select) LOW to choose the slave device.
Master generates the clock
  The master provides SCLK, which synchronizes data transfer between master and slave.
Data transfer happens on clock edges
  Data is sent from Master to Slave on MOSI and from Slave to Master on MISO, based on clock edges (CPOL/CPHA).
Communication ends by releasing SS
  After data transfer, the master sets SS HIGH, ending the SPI communication.
WORKING

## Slide 5
CPOL & CPHA TIMING DIAGRAM

## Slide 6
SPI MODES OF OPERATION
1.Run Mode (Normal Mode)
  SPI works normally
  Clock is ON
  Data transmission and reception occur as usual
  Used during regular operation
2. Wait Mode (Low-Power but Smart Mode)
Wait mode behavior depends on SPISWAI bit.
  If SPISWAI = 0, SPI behaves exactly like Run Mode, No power saving.
  If SPISWAI = 1, SPI clock generation is turned OFF to save power.
Master Mode
  Ongoing transmission pauses
  Transmission resumes when CPU returns to Run Mode
Slave Mode
  SPI continues receiving and transmitting
  This keeps the slave synchronized with the master

## Slide 7
SPI MODES OF OPERATION
3.Stop Mode (Deep Sleep Mode)
  Maximum power saving
  Master: Transmission stops, resumes in Run Mode
  Slave: Completes current byte and maintains synchronization

## Slide 8
MEMORY MAP/REGISTER DEFINITION
  This section describes the address space and registers used by the SPI module.

## Slide 9
SPI CONTROL REGISTER 1
SPIE – SPI Interrupt Enable
  Enables SPI interrupts
  Interrupt occurs when:
    SPIF (receive complete) OR
    MODF (mode fault) is set
Values:
  1 → SPI interrupts enabled
  0 → SPI interrupts disabled
SPE – SPI System Enable
  Turns the SPI module ON or OFF
  Assigns SPI function to port pins
Values:
  1 → SPI enabled, pins used for SPI
  0 → SPI disabled, low power, idle state

## Slide 10
SPTIE – SPI Transmit Interrupt Enable
  Enables interrupt when transmit buffer is empty (SPTEF)
Values:
  1 → SPTEF interrupt enabled
  0 → SPTEF interrupt disabled
MSTR – Master / Slave Select
  Selects SPI operating mode
Values:
  1 → Master mode
  0 → Slave mode

## Slide 11
CPOL – SPI Clock Polarity
  Selects the idle level of SPI clock (SCK)
  Master and Slave must use the same CPOL
  Changing CPOL during transmission aborts transfer
Values:
  CPOL = 0
    Clock idle = LOW
    Active-high clock
  CPOL = 1
    Clock idle = HIGH
    Active-low clock
CPHA – SPI Clock Phase
  Selects when data is sampled
  Master and Slave must use the same CPHA
  Changing CPHA during transmission aborts transfer
Values:
  CPHA = 0
    Data sampled on first (odd) clock edge
  CPHA = 1
    Data sampled on second (even) clock edge

## Slide 12
SSOE (SS Output Enable)
  Decides whether master drives SS or not
MODFEN = 0 (Mode-fault disabled)
SSOE Meaning
0 SPI does not use SS
1 SPI still does not use SS
MODFEN = 1 (Mode-fault enabled)
SSOE Meaning
0 SS is input (used for fault detection)
1 SS is output (master drives SS)

## Slide 13
LSBFE — LSB-First Enable
  Controls the bit transmission order in SPI communication
Operation
  LSBFE = 1
      Data is transferred Least Significant Bit (LSB) first
  LSBFE = 0
      Data is transferred Most Significant Bit (MSB) first

## Slide 14
SPI CONTROL REGISTER 2
MODFEN — Mode Fault Enable Bit
  Enables detection of Mode Fault (MODF) errors in SPI
  Controls how the SS (Slave Select) pin is used by the SPI module
Operation
  MODFEN = 1
      SS port pin is enabled with Mode Fault (MODF) detection
  MODFEN = 0
      SS port pin is not used by the SPI

## Slide 15
SPI CONTROL REGISTER 2
BIDIROE — Bidirectional Output Enable
  Controls the output buffer in bidirectional SPI mode
  Applicable only when bidirectional mode is enabled (SPC0 = 1)
Operation
  BIDIROE = 1
      Output buffer is enabled
  BIDIROE = 0
      Output buffer is disabled

## Slide 16
SPI CONTROL REGISTER 2
SPISWAI — SPI Stop in Wait Mode
  Used for power conservation when the CPU enters Wait Mode
  Controls whether the SPI clock runs or stops in Wait Mode
Operation
  SPISWAI = 1
      SPI clock generation is stopped in Wait Mode
      Helps reduce power consumption
  SPISWAI = 0
      SPI clock operates normally in Wait Mode
      No power saving

## Slide 17
SPC0 decides how many data pins SPI uses.
  SPC0 = 0 → Normal SPI mode
  SPC0 = 1 → Bidirectional SPI mode
SPI CONTROL REGISTER 2

## Slide 18
  Baud rate is determined by preselection bits (SPPR) and selection bits (SPR)
  Applicable only in Master Mode
Bit Function
  SPPR2–SPPR0
      Baud Rate Preselection bits
  SPR2–SPR0
      Baud Rate Selection bits
SPI BAUD RATE REGISTER

## Slide 19
  SPIF — SPI Interrupt Flag
  Indicates completion of a data transfer
  Set when a received data byte is copied into the SPI Data Register (SPIDR)
Operation
  SPIF = 1
      New data has been successfully received
      Data is available in SPIDR
  SPIF = 0
      Data transfer is not yet complete
SPI STATUS REGISTER

## Slide 20
  SPTEF — SPI Transmit Empty Interrupt Flag
  Indicates the status of the SPI transmit data register
  Used to control safe data transmission
Operation
  SPTEF = 1
      SPI Data Register is empty
      New data can be written to SPIDR
  SPTEF = 0
      SPI Data Register is not empty
      Write operation is not allowed
SPI STATUS REGISTER

## Slide 21
  MODF — Mode Fault Flag
  Indicates a mode fault condition in SPI operation
  Applicable when SPI is configured in Master Mode
Operation
  MODF = 1
      Mode fault has occurred
  MODF = 0
      No mode fault detected
SPI STATUS REGISTER

## Slide 22
  Single Data Register
      SPIDR acts as both input and output register for SPI data.
  Transmit Operation
      Writing to SPIDR queues one data byte for transmission.
      In Master mode, transmission starts immediately after the previous transfer completes.
  Transmit Ready Indication
      SPTEF flag in SPISR indicates when SPIDR is ready to accept new data.
  Receive Operation
      Received data can be read after SPIF is set and before the next transfer ends.
  Data Loss Condition
      If SPIF is not serviced before the next transfers complete,
  new data bytes are lost, and SPIDR retains only the first unread byte.
SPI DATA REGISTER

## Slide 23
THANK YOU