## Slide 1: AXI PROTOCOL
Boddu giresh chipweave technologies pvt ltd

## Slide 2: CONTENTS
Introduction to AXI features in AXI AXIchannels Interface&interconnect AXI signals
hand shake &burst transaction request attributes
01

## Slide 3: INTRODUCTION TO AXI
1.
Advance extensible interface it is a part of AMBA protocols it provides high perfomance ,high speed,high frequency protcol compared to APB/AHB
it is also supports a pipelined transcations
2.
02

## Slide 4: AXI FEATURES
Seperate Read/Write channels
High band width and low latency
Burst transactions
in order and out of order transactions 5. handshakeing mechanism
support out-standing and non-out standing transactions
pipelined transactions
04

## Slide 5: AXI CHANNELS
Write address channel (AW) Write data channel(W) Write response channel(B) Read address channel(AR) Read data channel(R)
05

## Slide 6: AXI CHANNELS
06

## Slide 7: INTERFACE&INTERCONNECT
a typical systems contents serval managers and subordinates connected together form of interconnect.
07

## Slide 8: SIGNALS WRITE CHANNEL
08

## Slide 9: SIGNALS OF READ CHANNEL
09

## Slide 10: HANDSHAKE MECHANISM
10

## Slide 11: BURST TRANSACTION
Burst means sending multiple data beats in a single address
There are 3 types of burst
Fixed
Increment
wrap

## Slide 12: FIXED:
The burst is used for repeat access to the simplification
The address is same for every transfer in the burst
The length of the burst can be upto 16 transfers

## Slide 13
INCREMENT:
The address is keep increasing for every transfer
Increment depend upon the transaction size
WRAPPING:
The address is increase but reaches the limit go back reverse address
The burst length must be 2,4,6,8, or 16 transactions

## Slide 14: TRANSACTION RESPONCE
Transaction response will be both read and write

## Slide 15: WRITE STROBE:
The write strobe carry that specify with byte of the write data channel contains valid information

## Slide 16: REQUEST ATTRIBUTES:
MEMORY ATTRIBUTES:
The memory attributes are request control and how transaction progress through a system and how caches handle the request

## Slide 17: MEMORY TYPES:
The combination of ARCACHE and AWCACHE signal indicate memory type

## Slide 18: THANK YOU