## Slide 1
AHB
BODDU GIRESH
CHIPWEAVE TECHNILOGIES PVT LTD

## Slide 2
INTRODUCTION TO AHB
  AHB(Advanced High Performance Bus) it is a AMBA family ,designed to support High performance, high bandwidth communication between different components in soc
  it is a multi master multi slave protoocl

## Slide 3
ARBITRATION
  Arbiter will decide which master can access the bus
  master will send request to arbiter by using (Hbusreq)
  arbiter will give premission 1 master at atime by using (Hgrant)

## Slide 4
COMPANY HISTORY
OUR
SIGNAL LIST OF AHB

## Slide 5
TYPES OF TRANSFER HTRANS[1:0]
HTRANS[1:0] Name Meaning
00 IDLE No transfer
01 BUSY Pause in a burst
10 NONSEQ First transfer
11 SEQ Remaining burst transfers

## Slide 6
TRANSFER SIZE HSIZE[2:0]
HSIZE[2] HSIZE[1] HSIZE[0] Size(bits) Description
0 0 0 8 Byte
0 0 1 16 Halfword
0 1 0 32 Word
0 1 1 64 Doubleword
1 0 0 128 Quad word
1 0 1 256 Octa word
1 1 0 512 Reserved
1 1 1 1024 Reserved
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore

## Slide 7
AHB BASIC READ/WRITE TRANSFER

## Slide 8
AHB WITH WAIT TRANSFER
MULTIPLE DATA TRANSFER

## Slide 9
BURST OPERATION HBURST[2:0]
  Burst means send multiple data beats(packets) in a single transfer
  Burst are two types
  increment burst
  wrapping burst

## Slide 10
HBURST[2:0]
HBURST Type Description
000 SINGLE Single transfer (no burst)
001 INCR Incrementing burst, undefined length
010 WRAP4 4-beat wrapping burst
011 INCR4 4-beat incrementing burst
100 WRAP8 8-beat wrapping burst
101 INCR8 8-beat incrementing burst
110 WRAP16 16-beat wrapping burst
111 INCR16 16-beat incrementing burst

## Slide 11
EXAMPLE
HIZE = 3'b010 HBRUST = 3'b011
4 Byte INCR4
INCREMENT BURST
The address keep increasing foreach new data transfer
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
4 beats(packets) in a burst
0x38 - 1beat
0x3C - 2beat
0x40 - 3beat
0x44 - 4beat

## Slide 12
WRAPPING
The address increases , but it reaches limit go back to start address
Wrap boundary
boundary = HSIZE X HBURST
example HSIZE = 1 BYTE HBURST = WRAP4
boundary = 1 x 4 => 4bytes
EXAMPLE
HISZE = 4 byte HBURST = WRAP4
wrap boundary = 4 x 4 => 16byte
Now your address
0x30 → 0x34 → 0x38 → 0x3C
but your address not start 0x00
it will start 0x38
0x38 → 0x3C → 0x30 → 0x34

## Slide 13
SLAVE RESPONSE SIGNALING HRESP[1:0]
The HRESP indicate the transfer in AHB response given by slave to master transfer is successful or not
HRESP Response Description
00 OKAY Transfer completed successfully
01 ERROR Transfer failed
10 RETRY Master should retry later
11 SPLIT Transfer split; master blocked until re‑granted

## Slide 14
OVERVIEW
we discuss the below topics
  introduction of AHB
  AHB signals
  AHB arbitration
  AHB types of transfers
  transfer size
  basic write/read transfers
  multiple transfers
  burst operations
  response signaling

## Slide 15
THANK YOU